## Slide 1
Design Features
Measured Performance
Show concrete, quantitative evidence that your device works. Show how, and to what degree, your design meets the key customer requirements. Plots, photos of the device in action, or tables of results would be good to add. However, do not cram too much information into the space
This is where you show your convincing evidence for the success of your project
Project Objective Statement
The goal of the EFS project is to design, build, and test an electric propellant feed system for the PSAS LV4 liquid fueled bi-propellant rocket engine prototype by June 6, 2017.
Key Customer Requirements
Design, build and test a technology development platform for the electronic propellant feed system.
Design a pump capable of delivering 350 psi of pressure at 11 GPM to the combustion chamber.
Pump performance characterization.
Scalable design for future pump iterations.
Open source documentation, design artifacts and build information.
Acknowledgments
Team Members: John C. Froehlich, Jonathan Talik, James Luce, Rawand Rasheed, Mimi Shang and Jordan Roland
Sponsor: Portland State Aerospace Society
Project Website
https://github.com/psas/electric-feed-system
Electric Propellant Feed System (EFS)
Motivation
Historically, the systems to impel propellants to the combustion chamber of a liquid fueled rocket are based on the employment of turbo-pumps or pressurized gas systems.
The complexity and cost of these methods has made building a liquid fuel rocket financially and technically difficult for the amateur rocket community.
By pursuing the open source development of an electric motor powered, high speed propellant feed system,
Future Work
Investigate additional design variations.
Test pump with PSAS pintle injector.
Adapt system for cryogenic propellants.
Scale design to match PSAS LV4 requirements.
Refine motor control and motor data acquisition.
Erin Schmidt Raúl Bayoán Cal Andrew Greenberg | Kris Auclair Mike Chung Haneef Mubarak
Water cooled 240 amp brushless DC motor
Load cell for live shaft torque measurement
Floating motor mount
Thrust and radial load bearings
Shaft seal and Rulon bushing
Inlet eye
Barske straight blade impeller
O-ring seal
Modular diffuser mount
Impellers
The EFS system uses an unorthodox Barske straight blade impeller to meet the unusually high head, low flow engine requirements. Final designs were 3D Printed in stainless steel.
Experimental Test Platform
Arduino microcontroller used for motor control and system data acquisition.
Variables monitored: Suction pressure, discharge pressure, volute and seal cavity pressures, RPM, flow rate, inlet temperature and shaft torque.
Constant inlet pressure (~45 psi) provided via a 42 gallon water tank.
Flow is controlled during testing using a gate valve on the discharge side.
Motor and speed controller water cooled .