## Slide 1
Portland State Aerospace Society | Electric Propellant Feed System
Notes: allowable test tolerances

## Slide 2
Open-ended literature review
Math is involved
Scientific computing
We make some guesses too
Notes: literature review to narrow the region of interest. (Don’t solve problems we don’t have to)
Scientific computing as an example of using tools to implement theory OR IDEAS. Matercam, SW, Python, Arduino
  Allows us to make calculations (OR DESIGNS) over a wide range of values and explore a little.
  We can iteratively develop
  note:
  Guessing is cheaper
  If best head coeff is between 0.5 and 1 we use 0.75 

## Slide 3
Visualize the Results
(If you can plot it, plot it!)
You are here
Parametric Design
(Design freedom)
Viola
(3D-Printed Stainless Steel)
Notes: FIRST
We visualize the results of the detailed design in many different ways. Road map
Now that the design is narrow enough we begin breathing life into it.
SECOND
We can play with the design and not leave theoretical and conceptual bounds. Entire geometry changes, casing changes, speed, power changes…
- Give example of Av rule to illustrate the impact of parametrization on success of project

## Slide 4: Performance Testing
Notes: Centrifugal pump is a complex turbomachine
Purely analytical prediction not possible
Hence, performance is obtained empirically

## Slide 5
Hydraulic Institute Test Standard (ANSI/HI 14.6 "Rotodynamic Pumps for Performance Acceptance Tests," 2011)
Using Hydraulic Test Standard (ANSI/HI 14.6)
Typically performance is given by curves of:
• Head versus capacity
• Power versus capacity
• NPSH versus capacity
Characterizing the performance of Piglet
Notes: We followed hydraulic standards intended to demonstrate hydraulic performance and mechanical integrity
• Head versus capacity
Using head and not pressure = head-capacity performance independent of the specific gravity of the liquid.
• Power versus capacity
BHP and WHP
• NPSH versus capacity
Lengthy description of value is unavoidable. Love to explain at the showcase
– Maximum head is at zero capacity
– The maximum capacity of the pump

## Slide 6
System Characteristics
Swamee-Jain Equation (1976)
Energy Equation
Explicit expression 10-6 < e/D, 10-2; 5000 < NR < 108
Notes: HEAD OF PUMP VS SYSTEM HEAD
The height to which a pump can raise the water is the pump head and it is measured in meters (feet) of flowing water. The head required to overcome the losses in a pipe system at a given flow rate is called the system head.
Using head and not pressure = head-capacity performance independent of the specific gravity of the liquid.
Energy equation
Each of these individual total heads = sum of the static pressure head, velocity head and elevation head.
That is, analyze the system to determine the pump head required as a function of flow rate through the pump … This will form the system line.
Plotting the pump curve and system curve will result in an intersection point, which is called the operating point.
Friction head
The friction head consists of the sum of the pipe friction head losses in the
Velocity head
Velocity head The velocity head is the kinetic energy contained in the water being pumped at any point in the system

## Slide 8
Figure: EFS model PIGLET-1 2.1in Diam. Impeller experimental results at 16500 rpm.
Centrifugal Pump Performance @ 16,500 rpm
Notes: The NPSH always rises as the centrifugal pump capacity approaches shut‑off (zero flow rate).
minimum value at a capacity Q about 40 percent of the best‑efficiency capacity

## Slide 9
Notes: A centrifugal pump is a very complex turbomachine, and purely analytical prediction of its performance is not possible. Hence, performance is obtained empirically.
Despite the low efficiency, regenerative ring pumps have several advantages over other turbomachines with similar tip speed due to relatively low manufacturing costs, simplicity, high reliability, enhanced priming behavior and can in many applications offer a more efficient alternative.

## Slide 10
Blade number affects efficiency and introduces circulatory losses (too few blades) and passage losses (too many blades)
Notes: operating the pump against close valve for a long time causes considerable damage on the pump since almost all the motor power is transformed into thermal energy which is absorbed by the pumped liquid.
Straight radial vane impeller in a single emission point
affinity laws should only be used for impeller trims of about 5 percent